## Slide 1: A Yang Data Model for Optical Impairment-aware Topology
Co-authors (editors):
Young Lee (SKKU)
Victor Lopez (Telefonica)
Gabriele Galimberti (Cisco)
Jean Luc Auge (Orange)
Dieter Beller (Nokia)
Co-authors/contributors:
Haomian Zheng (Huawei)
Italo Busi (Huawei)
Nicola Sambo (Scuola superior S.Anna)
Julien Meuric (Orange)
Esther Le Rouzic (Orange)
Sergio Belotti (Nokia)
Enrico Griseri (Nokia)
Gert Grammel (Juniper)
Jonas Martenson (RISE)
Aihua Guo (Huawei)
draft-ietf-ccamp-optical-impairment-topology-yang-02

## Slide 2: Major Activities since IETF 105
Weekly CCAMP WebEx meetings (Thu, 4-5pm CET)
Topics addressed:
  ROADM model:
    ROADM architectures discussed – outcome: new sections in version 02
    Modeling of optical impairments for ROADMs – starting with simple approach:
      Homogenous architecture
      3 paths identified: express path (pass-through), add path, and drop path
  3R regenerators – discussion started
    Two 3R regenerator realizations discussed
      Two back-to-back transponders
      Two transponders each providing uni-directional 3R regeneration

## Slide 3: ROADM modeling: express (through) path, add path, drop path
ROADM
OCX
OT Client Interfaces
Line east
Line west
OT
OT
Physical device
Ingress/egress amplifier modeled as part of TE link

## Slide 4: ROADM modeling
Ingress and egress amplifiers modeled as part of the TE link like in-line amplifiers (ILAs)
Agreed express, add, drop path impairment parameters (read-only):
  Chromatic dispersion (CD)
  Polarization mode dispersion (PMD)
  Polarization dependent loss (PDL)
Other impairment parameters still under discussion:
  Cross-talk due to imperfect optical isolation of components
  Filtering impacts – how to characterize and model filtering impacts

## Slide 5: Integrated ROADM architecture with integrated optical transponders (OTs) providing client interfaces
ROADM
OCX
OT
OT
OT
OT
OT Client Interfaces
Line east
Line west

## Slide 6: Integrated ROADMs with integrated OTs and single channel add/drop interfaces for remote OTs
ROADM
OCX
OT
OT
OT
OT
OT Client Interfaces
Line east
Line west
Colored OT Line Interfaces

## Slide 7: Disaggregated ROADMs that are subdivided into degree, add/drop, and optical transponder subsystems
Line 1
Degree 2
Degree 1
WSS
OT
OT
OT
OT
OT Client Interfaces
Colored OT Line Interfaces
WSS
Add/Drop 1
Add/Drop 2
Line 2
Colored OT Line Interfaces
Abstracted
ROADM
OCX

## Slide 8: 2 Optical Transponders (OTs) used as 3R regenerator Option 1: bi-directional back-to-back configuration
ROADM
OCX
OT Client Interfaces
Line east
Line west
OT
OT
2 OTs can only be used as 3R regenerators
Cable

## Slide 9: 2 Optical Transponders used as 3R regenerator Option 2: uni-dir 3R configuration (internal loop)
ROADM
OCX
Line east
Line west
OT
OT
2 OTs can be used as 3R regenerators or as service end-point OT (flexibility!)
Client Interface

## Slide 10: Major Changes since IETF 105
Text/figures added describing the ROADM architectures
YANG model remained unchanged – agreements still to be reached how to model optical impairments for ROADMs before the YANG model can be updated (TE topology augmentations for layer 0).

## Slide 11: YANG model and draft on GitHub
The authors/contributors are using GitHub:
  https://github.com/younglee-ietf/ietf-optical-impairment-yang
This is not a CCAMP WG “organization” GitHub account but it can still be used for the time being.
As suggested by the authors/contributors, the CCAMP chairs agreed to create a CCAMP WG “organization ”account as defined in:
  https://tools.ietf.org/html/draft-ietf-git-github-wg-configuration-03

## Slide 12: Open Issues - listed on GitHub https://github.com/younglee-ietf/ietf-optical-impairment-yang/issues

## Slide 13: Next Steps
Conclude on how to model the optical impairments for ROADMs:
  Cross-talk contributions to signal degradation (OSNR degradation)
  Identify the TE node entities (containers) in the TE topology YANG suitable for optical impairment augmentations (scalability!)
  Define the YANG model augmentations in the YANG module
  Study filtering impacts on signal quality and how to model those
Modeling of 3R regenerators
Address the other open issues on GitHub

## Slide 14: Thank You!